## Slide 1: CS 524 A
Introduction to Cloud Computing
Module 5: Data Networking and Distributed Computation (Part 1)

## Slide 2: Outline (Cloud Computing = Virtual Machines + Virtual Networks + Orchestration and Management)
Our topic is Networking
Two major topics
  Introduction to data communications and IP networks
  QoS in IP networks and multiprotocol “pipes”
  Network organization, peering, and pricing
Today we cover
  History (telegraph and telephone networks, Paul Baran’s work in RAND, PDN, PSDN, ISDN, Internet)
  The OSI Reference Model
  Link layer in Local Area Networks (“virtual LANs”—later )
  An introduction to the Internet

## Slide 3: Relation of the overall subject to Cloud Computing
IaaS provides both virtual machines and “pipes”
The Cloud is built on data networking
All cloud services are accessed via Internet Application Layer protocols (at run-time) and API (by the programmer)
We need data communications and distributed computing to understand
  how the Cloud is built
  what services the Cloud can provide
  how to access Cloud services

## Slide 4
Dual aspects of networking in Cloud Computing
Data
Network
Data
Network
a)
b)

## Slide 5
Private Network
Virtual Private Network
Another Virtual Private Network
Public
Network
Private and Virtual Private Networks
Private Network
Segment
Private Network
Segment

## Slide 6: How Do Machines Talk? The OSI Reference Model
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Network Layer
Link Layer
Physical Layer
Network Layer
Link Layer
Physical Layer
Host
Host
Process
Process
Router
Router

## Slide 7: Requests, Indications, and Protocols
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Link Layer
Physical Layer
Layer N+1
Layer N+1
Layer N
Layer N
req
ind
Layer N+1 Protocol
Layer N Protocol
Requests are typically implemented as procedure calls;
Indications are technically interrupts

## Slide 8
Figure 4.4: Requests and Indications as methods in the Layer Class
Header | Payload
Protocol Data Unit
Request (called by the layer above)
Indication(called by the layer below)

## Slide 9
Figure 4.5: Summary of the overall computational model
The networking-device-facing layer
The application-process-facing
layer
From the networking device
Interrupt service routine
To the networking device handler
(The main line)
The application-supplied
plug-in routine
Application Process
Indication flow
Request flow

## Slide 10: Protocol Frame Format
Layer 2 Header | Layer 3 Header | ... | Layer N Header | Protocol Data Unit (PDU)
1110010011000100100001001001001000100010001000100010011111001001110
Layer 1 (Physical layer) just produces a bit stream

## Slide 11: The Physical Layer
The Physical layer is concerned with transmitting “0”s and “1”s
It knows how to establish the connection (in case of modems and telephone lines) or avoid collisions (in case of Ethernet-like networks)
It has to know how voltages or light bursts are mapped into binary digits
0 0 0 1 0…
1 0 1 1 1 0 0…

## Slide 12
Broadcast media configurations
Bus
A B C D E
Star
Wireless
Ring
NB: The dangers of the promiscuous mode

## Slide 13: The Data Link Layer
The data link layer is responsible for framing the 1s and 0s of the Physical Layer
In some cases it is also responsible for guaranteeing delivery (so it needs checksums and other error detection [or error correction] mechanisms as well as retransmission of the garbled packets)
Thus the data link protocol often involves the mechanisms for requesting retransmission

## Slide 14: Network Layer
The network layer may establish a circuit (in the case of connection-oriented protocols), or it may simply send its datagrams—probably repeating them—in the directions determined by the forwarding mechanisms
The network layer elements have to know the topology of the network, which is determined through the routing protocol
The network layer may also break larger messages into smaller ones
The network layer entities (routers) have routing and forwarding as their two major functions

## Slide 15: Local Area Networks (LANs)
LANs are privately owned (within a building or campus)
LANs are characterized by
  size (up to five kilometers)
  transmission technology (e.g., bus, wireless, star, or ring)
  speed (10 to 100 megabits per second [mbps])
  physical and link-layer protocols standardized in the IEEE 802.* series of standards
LANs can be connected by Layer 2 switches

## Slide 16: Metropolitan Area Networks (MANs)
MANs are simply bigger LANs (covering a group of offices in the campus)
MANs characteristics are similar to those of LANs
MANs may contain Layer 2 switching elements (in addition to media transmission elements!

## Slide 17: Wide Area Networks (WANs)
WANs span large geographic areas
WANs consist of user computers (hosts or endpoints) attached to subnets
Subnets are interconnected by means of routers and transmission lines
It is possible—we will talk about it in the next lecture—to provide WANs as virtual LANs, and this is something the Cloud can do!

## Slide 18: Wide Area Networks (WANs)
Router
Host
LAN
Remote access

## Slide 19: Transport Layer
The transport layer is concerned with delivering messages from one host to another
The transport layer service can be reliable (in which cases both the delivery as well as delivery in sequence are guaranteed) or unreliable
In the Internet, the Transmission Control Protocol (TCP) provides a reliable service, while the User Datagram Protocol (UDP) provides unreliable service

## Slide 20: Session Layer
The session layer is an enhanced (process-to-process) version of the connection-oriented transport layer
It provides dialog control and synchronization facilities
It has been implemented in SNA and a varieties of old ISO-based architectures, but it is not named absent in the Internet suite, where TCP is actually doing the job of both the transport and session layers

## Slide 21: Presentation Layer
The presentation layer is concerned with the semantics of the message
The presentation layer ensures, for example, that the byte layout of the sending machine is properly translated into that of the receiving machine
Earlier applications of the presentation layer involved translating from one set of character representations into another (like ASCII into EBCDIC and vice versa)
The transmission of the integers, sets, and other data structures can also be taken care of by the presentation layer

## Slide 22: The Application Layer
Early application layer protocols in the Internet were the File Transfer Protocol (FTP), Simple Mail Transfer Protocol (SMTP), and Directory Services Protocol (DSP)
But the HyperText Transfer Protocol (HTTP) has become the protocol of choice for almost everything on the Web (we will talk more and more… and more about that)!
And now the Internet hourglass:

## Slide 23: Introduction to the Internet (outline)
Definition and basic principles
Routing in the Internet
The Internet protocol stack

## Slide 24: The Internet
In general,
An internet is a collection of interconnected networks (typically, Local Area Networks [LANs], Metropolitan Area Networks [MANs], and Wide Area Networks [WANs] governed by the Internet Standards
Specifically,
the Internet is a… world-wide internet that is widely used to connect university, government offices, companies and private individuals. (A. S. Tanenbaum, “Computer Networks”)

## Slide 25: Internet Standardization
Internet standards are produced (by consensus) by the Internet Engineering Task Force (IETF)
Anyone can participate in the IETF by joining a mailing list of a working group: there is no fee
All IETF documents and standards are available at its web site (www.ietf.org) at no charge
Internet Society is a legal umbrella of the IETF

## Slide 26
The Internet
...
IP Network 4
IP Network 3
IP Network 2
IP Network 1
Gateway
Gateway
Gateway

## Slide 27: The Internet Protocol (IP): the Glue of the Internet
IP packets (datagrams) specify the version of the protocol, time-to-live, source and destination addresses, options (e.g., security), and some other header-related information
Within the network layer packets are unacknowledged
IP (RFC 791) is an Internet Standard

## Slide 28
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
Version |  |  |  | IHL |  |  |  | Type of Service |  |  |  |  |  |  |  | Total length (in bytes) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Identification (common to all fragments) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Flags |  |  | Fragment offset |  |  |  |  |  |  |  |  |  |  |  | 
Time-to-live |  |  |  |  |  |  |  | Protocol |  |  |  |  |  |  |  | Header Checksum |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Source Address |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Destination Address |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Options (0 to maximum length) … |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Padding |  |  |  | 
The IPv4 Packet Header
(After RFC 791)

## Slide 29: IP Addresses (IPv4)
IP addresses are assigned to all hosts and routers
All IP addresses are 32-bit-long; they are normally written in decimal form byte-by-byte, separated by “.”s (e.g., 123.100.86.35)
Each address has a form of either
  <class> <network> (for classes A [0], B [10], and C [110]) or
  1110 <Multicast Address> (for class D [1110]) or
  11110 <Reserved for future use>
  And there is Anycast (please read RFC 4786 http://tools.ietf.org/html/rfc4786 and RFC 4193 for IPv6 addresses)

## Slide 30
Autonomous System
Host
Interior
Routing
Gateway
Exterior
Routing
Gateway
Routing protocol classification
a) LAN: No routing needed
b) Routing within and among the Autonomous systems
Autonomous System
Autonomous System

## Slide 31: Internet Architectural Principles (RFC1958)
Emphasize intelligence at the edges, distributed processing, dynamic (versus static) solutions, and modularity
Support accommodation of multiple network types
Are not a religion (RFC 1958 is informational)
Are inherently hostile to the needs of Internet-wide IP telephony or other applications not envisioned as the Internet ones

## Slide 32: Routing in the Internet
Network is a graph: routers (vertices) and links connecting routers (edges)
Links are assigned weights according to a metric
With Open Shortest Path First (OSPF) (RFC 2328), routers exchange the information on all links, compute shortest paths and construct forwarding tables with the next hop for each destination. OSPF is typically used within an Autonomous System (AS)
With the Border Gateway Protocol (BGP) (RFC 1772), ASs are effectively the vertices of the routing graph

## Slide 33: Autonomous Systems
Boundary
Routers
AS
AS
AS
Notes: BGP is executed by the boundary routers on behalf of ASs

## Slide 34
Physical
Link
Network
Transport
Optical, Ethernet, Wireless, twisted pair…
PPP, HDLC, SDLC, LAN LLC, AALs…
IP
UDP, TCP
SCTP
RTCP: Real Time Control Protocol
SDLC: High? Data Link Control
SMTP: Simple Mail Transfer Protocol
SCTP: Stream Control Transmission Protocol
SIP: Session Initiation Protocol
TCP: Transmission Control Protocol
UDP: User Datagram Protocol
Application
TELNET, FTP, RPC,
HTTP, SIP, RTP, RTCP, SMTP,
Diameter, WebSocket..
AAL: ATM Adaptation Layer
HTTP: Hyper Text Transfer Protocol
HDLC: High? Data Link Control
LLC: Logical Link Control
PPP: Point-to-Point Protocol
RPC: Remote Procedure Call
RTP: Real Time Protocol
The Internet Protocol Hourglass
(after Steve Deering)